## Slide 1: Learn to Program via Visual Programming and micro:bit
A Study Notes

## Slide 2: Outline
Intent
What is Visual Programming?
Visual Programming for Learning
IoT Devices and micro:bit
Visual Programming for micro:bit

## Slide 3: Intent
To walk-thru a visual programming environment for learning multiple programming languages
  JavaScript
  Python
  Not cover here
  C/C++
  Lua, …

## Slide 4: Visual Programming
In computing, a visual programming language (VPL) is any programming language that lets users create programs by manipulating program elements graphically rather than by specifying them textually. A VPL allows programming with visual expressions, spatial arrangements of text and graphic symbols, used either as elements of syntax or secondary notation.
From [wikipedia](https://en.wikipedia.org/wiki/Visual_programming_language )

## Slide 5: Different Types
Computer Programming paradigms
  OO, flow-based, …
Programming stage
  conceptual, modeling, algorithm, ...
Application Domains
  finance, embedded system, education, multimedia, …
System Automation
  process, UI, logic validation, …

## Slide 6: micro:bit (1/2)

## Slide 7: micro:bit (2/2)
micro:bit is an ARM-based embedded system designed by the BBC for use in computer education in the UK, released in February 10th 2016.
The board is 4 cm × 5 cm and has
  an ARM Cortex-M0 processor,
  powered by either USB or an external battery pack.
Input/Output, Interface
  three ring connectors (plus one power one ground) which accept crocodile clips or 4 mm banana plugs
  a 23-pin edge connector with two or three PWM outputs, six to 17 GPIO pins (depending on configuration), six analog inputs, serial I/O, SPI, and I²C.
  accelerometer and magnetometer sensors,
  Bluetooth and USB connectivity,
  a display consisting of 25 LEDs, two programmable buttons one reset button.
Software
  Programming Language: Javascript, micropython, C/C++, TouchDevelop, Free Pascal
  Editor: [pxt](https://makecode.microbit.org/) based on Blockly for JavaScript, [mu](https://www.microbit.co.uk)

## Slide 8: JavaScript Cheat Sheet

## Slide 9: MicroPython Summary (supporting library)
array: numeric data arrays
builtins: basic functions
cmath: mathematical functions for complex numbers
gc: garbage collector
math: mathematical functions
select: wait for events on a set of streams
sys: system specific functions
ubinascii: binary/ASCII conversions
ucollections: collection and container types
uhashlib: hashing algorithm
uheapq: heap queue algorithm
uio: input/output streams
ujson: JSON encoding and decoding • uos: basic “operating system” services
ure: regular expressions
usocket: socket module
ustruct: pack and unpack primitive data types
utime: time related functions
uzlib: zlib decompression
uctypes: access binary data in a structured way
[Micropython differences from cpython](https://docs.micropython.org/en/latest/pyboard/genrst/index.html )

## Slide 10: Schematic, Breadboard, and Wiring

## Slide 11: Block and Script in PXT Editor

## Slide 12: Microsoft Touch Develop Example Using the Accelerometer to Control Motor Speed

## Slide 13: MicroPython Example in Mu Editor open file:///Users/rkuo/code/PythonEditor/editor.html

## Slide 14: Review
Gain
Improve understanding of
  Visual Programming Language,
  JavaScript, Python.
Gain some hands-on experience on
  Microcontroller, sensor, wiring.
Improve knowledge
  Prototyping software.
Discover ESP32 microcontroller
Plan
Component design in Node-Red, Blockly, App-Inventor.
Domain specific visual programming: data analytics.
Automation control

## Slide 15: Supplement Slides

## Slide 16: Node-Red

## Slide 17: AppInventor

## Slide 18: ESP8266 (https://en.wikipedia.org/wiki/ESP8266)
32-bit RISC CPU: Tensilica Xtensa L106 running at 80 MHz*
64 KiB of instruction RAM, 96 KiB of data RAM
External QSPI flash: 512 KiB to 4 MiB* (up to 16 MiB is supported)
IEEE 802.11 b/g/n Wi-Fi
  Integrated TR switch, balun, LNA, power amplifier and matching network
  WEP or WPA/WPA2 authentication, or open networks
16 GPIO pins
SPI
I²C
I²S interfaces with DMA (sharing pins with GPIO)
UART on dedicated pins, plus a transmit-only UART can be enabled on GPIO2
10-bit ADC (this is a Successive Approximation ADC)
The successor to these microcontroller chips is the ESP32.